## Slide 1
Temperature coefficient α
Buda Tech
Resistance at
α Temperature Coefficient
Resistance at
Final temperature
Temperature at 20°C or 0°C

## Slide 2
Temperature coefficient of Resistance α
Buda Tech
(α) Constant is known as the temperature coefficient of resistance and symbolizes the resistance change factor per degree of temperature change.
as all materials have a certain specific resistance (at 20° C), they also change resistance according to temperature by certain amounts.
For pure metals, this coefficient is a positive number, meaning that resistance increases with increasing temperature.
For the elements carbon, silicon, and germanium, this coefficient is a negative number, meaning that resistance decreases with increasing temperature.

## Slide 3
Temperature coefficient of Resistance α
Buda Tech
For some metal alloys, the temperature coefficient of resistance is very close to zero, meaning that the resistance hardly changes at all with temperature variations (a good property if you want to build a precision resistor out of metal wire!)

## Slide 4
Temperature coefficient of Resistance α
Buda Tech

## Slide 5
Temperature coefficient of Resistance α
Buda Tech
Why resistance of metallic substances increases with an increase in temperature?
The metals have free electrons moving randomly in the crystal structure. With an increase in temperature, the random motion of free electrons and inter-atomic vibration increase, and as a result, the collision rate between electrons inside the metal increases.

## Slide 6
Temperature coefficient of Resistance α
Buda Tech
Why resistance of metallic substances increases with an increase in temperature?
The increased collision rate impedes the flow of the electron through the metal, and thus, the resistance of the metal increases. Therefore, the temperature coefficient of the metals is positive.
Contrary to metallic substance, the resistance of the semiconductor and insulator substances decrease with an increase in temperature. The semiconductor and insulator material has a negative temperature coefficient..

## Slide 7
Temperature coefficient of Resistance α
Buda Tech
Why resistance of non-metallic substances decrease with an increase in temperature?
With an increase in temperature, the heat energy in the crystal increases, and as a result, the covalent bonds start breaking and releasing more electrons in the crystal. Now, more electrons leave the valence band, pass through the forbidden gap, and reach the conduction band.

## Slide 8
Temperature coefficient of Resistance α
Buda Tech
Why resistance of non-metallic substances decrease with an increase in temperature?
The number of free electrons reaching from the valence band to the conduction band increases with an increase in the temperature. Hence, the resistance of the non-metallic substance decreases with an increase in temperature.

## Slide 9
Temperature coefficient of Resistance α
Buda Tech
Resistance of a conductor at usually 20 °C or sometimes 0 °C
α Conductor Temperature Coefficient / °C
Resistance at
Conductor Temperature Coefficient in °C

## Slide 10
Temperature coefficient of Resistance α
Buda Tech
Example
A sample of copper has a resistance of 10Ω at a temperature of 0°C. What will be
its resistance at 50°C?
= 10
α 0.00404/ °C
= ??
= 50°C
= 0°C

## Slide 11
Ω
Temperature coefficient of Resistance α
Buda Tech
Example
A sample of copper has a resistance of 10Ω at a temperature of 0°C. What will be
its resistance at 50°C?
= 10
α 0.00404/ °C
= ??
= 50°C
= 0°C

## Slide 12
Temperature coefficient of Resistance α
Buda Tech
Example
A length of tungsten filament wire has a resistance of 200Ω at 20°C. What will be
its resistance at 600°C ( α = 0.0045 Ω / Ω /°C)?
= 200
α 0.0045/ °C
= ??
= 600°C
= 20°C

## Slide 13
Ω
Temperature coefficient of Resistance α
Buda Tech
Example
A length of tungsten filament wire has a resistance of 200Ω at 20°C. What will be
its resistance at 600°C ( α = 0.0045 Ω / Ω /°C)?
= 200
α 0.0045/ °C
= ??
= 600°C
= 20°C

## Slide 14
Temperature coefficient of Resistance α
Buda Tech
Example
The resistance of a bulb filament is 112Ω at a temperature of 110°C. and its resistance is 180Ω at 375 °C. Calculate its temperate coefficient.
= 112
= 110°C
α = ??
= 180
= 375°C
0°C
---------(equation 1)
---------(equation 2)

## Slide 15
Temperature coefficient of Resistance α
Buda Tech
Example
The resistance of a bulb filament is 112Ω at a temperature of 110°C. and its resistance is 180Ω at 375 °C. Calculate its temperate coefficient.
= 112
= 110°C
α = ??
= 180
= 375°C
0°C
---------(equation 1)
---------(equation 2)

## Slide 16
Temperature coefficient of Resistance α
Buda Tech
---------(equation 1)
---------(equation 2)
=

## Slide 17
Temperature coefficient of Resistance α
Buda Tech
1.6 =

## Slide 18
Temperature coefficient of Resistance α
Buda Tech
1.6 =
1.6 =
1.6 + 176 = 1 +
1.6 - 1 = - 176
0.6 = 199

## Slide 19
Temperature coefficient of Resistance α
Buda Tech
1.6 + 176 = 1 +
1.6 - 1 = - 176
0.6 = 199
=
= 0.003015Ω/Ω/°C

## Slide 20
Temperature coefficient of Resistance α
Buda Tech
Example
The resistance of a bulb filament is 100Ω at a temperature of 100°C. If its TCR is 0.005 per °C, its resistance will become 200Ω at a temperature of?
= 100
= 100°C
α = 0.005Ω/Ω/°C
= 200
= ?
0°C

## Slide 21
Temperature coefficient of Resistance α
Buda Tech
---------(equation 1)
---------(equation 2)
=

## Slide 22
Temperature coefficient of Resistance α
Buda Tech
---------(equation 1)
---------(equation 2)
=

## Slide 23
Temperature coefficient of Resistance α
Buda Tech
2 =
3 = 1 +
2=

## Slide 24
Temperature coefficient of Resistance α
Buda Tech
2 =
3 = 1 +
3 - 1 =
2 =
=
= 400°C
2=